## Slide 1: K-Maps

## Slide 2: Simplify - F(A,B,C) = m2 + m3 + m6 + m7
Notes: F= A’C +B’C

## Slide 3: Boolean Function Optimization
Minimizing the gate input (or literal) cost of a (a set of) Boolean equation(s) reduces circuit cost.
We choose gate input cost.
Boolean Algebra and graphical techniques are tools to minimize cost criteria values.
Some important questions:
  When do we stop trying to reduce the cost?
  Do we know when we have a minimum cost?
Treat optimum or near-optimum cost functions for two-level (SOP and POS) circuits first.
Introduce a graphical technique using Karnaugh maps (K-maps, for short)

## Slide 4: Karnaugh Maps (K-map)
A K-map is a collection of squares
  Each square represents a minterm
  The collection of squares is a graphical representation of a Boolean function
  Adjacent squares differ in the value of one variable
  Alternative algebraic expressions for the same function are derived by recognizing patterns of squares
The K-map can be viewed as
  A reorganized version of the truth table
  A topologically-warped Venn diagram as used to visualize sets in algebra of sets

## Slide 5: K-map
Notes: Adjacent cell varies only one place either horizontal or vertical

## Slide 17: Two Variable Maps
A 2-variable Karnaugh Map:
  Note that minterm m0 and
  minterm m1 are “adjacent”
  and differ in the value of the
  variable y
  Similarly, minterm m0 and
  minterm m2 differ in the x variable.
  Also, m1 and m3 differ in the x variable as well.
  Finally, m2 and m3 differ in the value of the variable y
y = 0
y = 1
x = 0
m
0 =
m
1 =
x = 1
m
2 =
m
3 =
y
x
y
x
y
x
y
x

## Slide 18: Three Variable Maps
A three-variable K-map:
Where each minterm corresponds to the product terms:
Note that if the binary value for an index differs in one bit position, the minterms are adjacent on the K-Map
yz=00
yz=01
yz=11
yz=10
x=0
m0
m1
m3
m2
x=1
m4
m5
m7
m6
yz=00
yz=01
yz=11
yz=10
x=0
x=1
z
y
x
z
y
x
z
y
x
z
y
x
z
y
x
z
y
x
z
y
x
z
y
x