## Slide 1: Clock, S-R Flipflop, D Flipflop

## Slide 2
Clock
Clock
a periodic external event (input)
synchronizes when current state changes happen
keeps system well-behaved makes it easier to design and build large systems
External Input to control the circuit

## Slide 3: S-R Latch with control input/ S-R flip Flop
Occasionally, desirable to avoid latch changes
C = 0 disables all latch state changes
Control signal enables data change when C = 1
Right side of circuit same as ordinary S-R latch.

## Slide 4: D Flip Flop
Q
Q’
C
D
S
R
S R C Q Q’
0 0 1 Q0 Q0’ Store
0 1 1 0 1 Reset
1 0 1 1 0 Set
1 1 1 1 1 Disallowed
X X 0 Q0 Q0’ Store
0 1 0 1
1 1 1 0
X 0 Q0 Q0’
D C Q Q’
Q0 indicates the previous state (the previously stored value)

## Slide 5: D Flip Flop
Q
Q’
C
D
S
R
X
Y
0 1 0 1
1 1 1 0
X 0 Q0 Q0’
D C Q Q’
Input value D is passed to output Q when C is high
Input value D is ignored when C is low

## Slide 6: D Flip-Flop
C
D
Latches on following
edge of clock
C
D
Q
C
D
Q
Q
Q only changes when C is high
If C is high, Q will follow D
The D latch stores data indefinitely, regardless of input D values, if C = 0
Forms basic storage element in computers

## Slide 7: Verilog
module D_FF(D, Clk, Q, Qbar);
input D, Clk;
output Q, Qbar;
always @ (D or Clk) //sensitivity list
  if(Clk)
  begin
  Q <= D;
  Qbar <= ~D;
  end
endmodule

## Slide 8: Symbols for Latches
SR latch is based on NOR gates
S’R’ latch based on NAND gates
D latch can be based on either.
D latch sometimes called transparent latch